## Slide 1
⚡ VISIONPILOT
AI-Assisted RC Car Controller
ESP32 · L298N · Servo · VL53L0X · MPU-6050 · GPS · Flutter APK
HackTheHardware 2.0 · 2026

## Slide 2
PROJECT OVERVIEW
What VisionPilot does
VisionPilot turns a cheap RC car into a wirelessly-controlled robot with real-time sensor feedback, safety interlocks, and a custom Android app — all built from scratch in 48 hours.
Key Features
• WiFi UDP control at 20 Hz (< 50ms latency)
• Dual-joystick Android app (Flutter APK)
• Servo steering + DC motor speed control
• Hardware watchdog: stops on link drop
• Bumper interlock: locks fwd on collision
• Kill / Clear commands from the phone
• Live battery voltage + car state telemetry
Hardware Stack
• ESP32 Dev Board (240 MHz, WiFi)
• L298N H-bridge motor driver
• Hobby servo for steering (GPIO13)
• VL53L0X ToF sensor (obstacle range)
• MPU-6050 IMU (accel + gyro)
• GY-NEO6MU2 GPS module
• 3x RAMPS bumper endstops
• 7.4V LiPo + 5V buck converter
• Samsung S24 running Flutter APK

## Slide 3
SYSTEM ARCHITECTURE
Communication and control flow
ANDROID APP
(Flutter)
Dual Joystick UI
ESP32 FIRMWARE
(Arduino)
UDP + State Machine
ACTUATORS
DC Motor (L298N)
Servo Steering
SENSORS
VL53L0X · MPU-6050
GPS · Bumpers
PHONE DISPLAY
Status · Battery
Bumper state
UDP port 4210 (D/K/C commands) · UDP port 4211 (T telemetry) · 20Hz drive loop · 300ms watchdog

## Slide 4
UDP CONTROL PROTOCOL
Text-based, stateless, sub-50ms latency
Commands (Phone → Car, port 4210)
• D,<seq>,<throttle>,<steer>
• seq — monotonic sequence number
• throttle — -100..+100 (neg=reverse)
• steer — -100..+100 (neg=left)
• K — KILL (immediate full stop)
• C — CLEAR (release kill/bumper lock)
• Sent at 20 Hz by Timer.periodic
• Out-of-order packets dropped (seq)
Telemetry (Car → Phone, port 4211)
• T,<seq>,<mask>,<mV>,<state>
• mask — bumper bits L=1 C=2 R=4
• mV — battery millivolts
• state — 0=OK 1=WD 2=BUMPER 3=KILL
• Sent every 100ms
• Dest: source IP of last D packet
• State machine:
• OK → normal drive
• WD → no packet >300ms → stop
• BUMPER → fwd blocked until reverse
• KILL → full stop until CLEAR

## Slide 5
ESP32 FIRMWARE
visionpilot_esp32.ino · Arduino Core 3.x
WiFi AP Mode
• ESP32 creates its OWN WiFi network
• SSID: VisionPilot Pass: vp123456
• IP always 192.168.4.1
• Phone joins car's WiFi directly
• No router / hotspot needed
• ensureWifi(): returns udpStarted in AP
Motor & Servo PWM
• ledcAttachChannel() — Arduino 3.x API
• Motor: ch0 · 1kHz · 10-bit · GPIO25
• Servo: ch2 · 50Hz · 16-bit · GPIO13
• Speed map: 35%-100% duty range
• Direction: IN1/IN2 digital H-bridge
Safety Interlocks
• Watchdog: no packet >300ms → stop
• Bumper lock: hit → fwd disabled
• Unlock: reverse off + C from phone
• Kill latch: K packet → full stop
• All states reported in telemetry
Sensor Reads
• Bumpers: digitalRead + PULLUP
• Battery: analogReadMilliVolts x3.128
• VL53L0X: I2C addr 0x29
• MPU-6050: I2C addr 0x68
• GPS: Serial2 9600 baud NMEA

## Slide 6
ANDROID CONTROL APP
Flutter · Dart · UDP · Dual Joystick · APK via ADB
car_socket.dart
• RawDatagramSocket (dart:io)
• Send to car 192.168.4.1:4210
• Listen port 4211 for telemetry
• Timer.periodic 20Hz drive loop
• sendDrive(throttle, steer)
• sendKill() / sendClear()
• Stream<Telemetry> broadcast
joystick_widget.dart
• GestureDetector + CustomPaint
• Bounded circular drag area
• 5% dead-zone at center
• Thumb snaps to center on release
• onChanged(dx, dy): -1.0..1.0
• Left Y-axis → throttle
• Right X-axis → steer
Build & Deploy
• Settings: IP + port persisted
• SharedPreferences storage
• flutter build apk --release
• adb install app-release.apk
•
• Permissions:
• INTERNET
• ACCESS_WIFI_STATE
• CHANGE_WIFI_MULTICAST_STATE

## Slide 7
WIRING SUMMARY
ESP32 GPIO pin assignments
GPIO
Connected To
Signal Type
Notes
GPIO 25
L298N ENA
PWM 1kHz
Motor speed (remove ENA jumper!)
GPIO 26
L298N IN1
Digital OUT
Motor direction A
GPIO 27
L298N IN2
Digital OUT
Motor direction B
GPIO 13
Servo SIG
PWM 50Hz
Steering 1100-1900µs center 1500
GPIO 32
Bumper LEFT
INPUT_PULLUP
Active LOW when pressed
GPIO 33
Bumper CENTER
INPUT_PULLUP
Active LOW when pressed
GPIO 14
Bumper RIGHT
INPUT_PULLUP
Active LOW when pressed
GPIO 35
Battery ADC
ADC1_CH7
100kΩ+47kΩ divider ×3.128
GPIO 21
SDA
I²C
VL53L0X(0x29)+MPU-6050(0x68) shared
GPIO 22
SCL
I²C
Shared I²C bus
GPIO 16
GPS TX→RX
UART2 RX
9600 baud NMEA
GPIO 17
GPS RX←TX
UART2 TX
9600 baud
GPIO 2
Built-in LED
Digital OUT
Solid=OK fast-blink=no link

## Slide 8
DEMO RESULTS
What we built and tested successfully
Successfully Demonstrated
• ESP32 flashed via arduino-cli (headless)
• WiFi AP 'VisionPilot' visible on phone
• Samsung S24 joined car's WiFi network
• Flutter APK installed via ADB
• App shows green 'OK' status
• Live battery voltage in app UI
• Left joystick → DC motor fwd/rev
• Right joystick → servo steering
• KILL button → immediate car stop
• CLEAR resumes normal drive
• Bumper interlock working correctly
• Watchdog stops car on app close
Critical Bug Fixed
• AP mode: WiFi.status() never returns
• WL_CONNECTED (ESP32 IS the AP)
• ensureWifi() always returned false
• Fix: #if USE_AP_MODE return udpStarted
• After reflash: app showed OK instantly
Build Challenges Solved
• USE_AP_MODE (SDK enum conflict fix)
• ESP32 bootloader: manual BOOT+EN
• Flash baud 921600→115200 for stability
• ADB sideload without manual transfer

## Slide 9
NEXT STEPS
Future development roadmap
App Enhancements
• Integrate into main codebase
• OTA firmware update from app
• GPS live map on phone screen
• Record and replay drive paths
• Autonomous follow mode UI
• Obstacle avoidance overlay
Firmware Features
• VL53L0X obstacle avoidance
• MPU-6050 traction/stability
• GPS waypoint following
• PID speed controller
• Explore and replay brain
• ESP32-CAM video stream
Infrastructure
• Custom PCB for clean wiring
• 3D printed sensor mounts
• LiPo charge indicator
• GitHub Actions CI build
• Unit tests for state machine
• Docker dev environment

## Slide 10
THANK YOU
VisionPilot — Built at HackTheHardware 2.0
ESP32 · Flutter · UDP · L298N · Servo · VL53L0X · MPU-6050 · GPS
Questions?